## Slide 1
Surface Dipole Library
A fast pre-screening tool for thin-film interface interactions
Calculates dipole moments & dipole–dipole interaction energies between surface atoms of a substrate and a thin film
Shubham Gangwar | Department Project | 2026
v 1.0.0

## Slide 2
Presentation Agenda
01
The Problem — Why this library was needed
02
Library Architecture — How it was built
03
What It Calculates — Key quantities
04
Input Requirements — What you need to provide
05
How to Get the Inputs — Coordinates & Charges
06
Formulas & Calculation Flow — Step by step
07
Output & Results — What the library returns
08
Case Study — Borosilicate Glass vs. TiO₂
09
Actionable Findings — What the results mean
10
Conclusion & Future Work

## Slide 3
The Problem
Why was this library needed?
Without This Library
✗ DFT calculation per config: 6–8 hours
✗ Screening 132 pairs = 3–5 days on HPC
✗ No guidance on which atoms to focus on
✗ Chemical intuition often wrong
✗ Expensive compute budget wasted on non-dominant pairs
With This Library
✓ All 132 pairs evaluated: < 1 second
✓ Dominant pair identified instantly
✓ Atomic-level resolution — exact sites
✓ Physically grounded (force-field charges)
✓ Reduces DFT workload by 90–95%
VS

## Slide 4
Library Architecture
7-module Python package
atoms.py
Atom dataclass with labelling helpers
dipole.py
calculate_dipole() atomic_local_dipole()
geometry.py
distance() pairwise_distances()
interaction.py
dipole_dipole_energy() SI-derived, eV
ranking.py
rank_interactions() print_summary()
io.py
XYZ / CIF / POSCAR ASE / Pymatgen readers
main.py
analyze_surface_interactions() high-level API
User Input → io.py → atoms.py → dipole.py → geometry.py → interaction.py → ranking.py → main.py → Results
__init__.py — re-exports everything via from surface_dipole_library import ...
# Install pip install surface-dipole-lib # Import from surface_dipole_library import analyze_surface_interactions
Requirements
Python ≥ 3.8 numpy pandas ase (optional, for CIF/POSCAR) pymatgen (optional, for oxidation states)
pyproject.toml included — pip-installable package

## Slide 5
What the Library Calculates
Three core quantities
1. Group Dipole Moment
μ = Σᵢ qᵢ rᵢ A single vector summarising how polar each surface is overall. Output: (μx, μy, μz) in e·Å and Debye
2. Local Atomic Dipole
μᵢ = qᵢ (rᵢ − r̄) The dipole contribution of each individual atom relative to the group centroid. Makes calculation origin-independent.
3. Dipole–Dipole Interaction Energy
U = 14.3996 × [μ₁·μ₂/r³ − 3(μ₁·r)(μ₂·r)/r⁵] Computed for every substrate–film atom pair. Ranked from most attractive to most repulsive. Output: Energy in eV, labelled attractive/repulsive

## Slide 6
Input Requirements
What you must provide per atom
①
Element Symbol
e.g. "Si", "Ti", "O", "Al", "Zn" Identifies which atom it is. Used for labelling and output tables.
②
3D Position (Å)
e.g. [0.00, 0.00, 1.60] Cartesian coordinates in Ångströms. Both surfaces must share the same coordinate system (same z-axis).
③
Partial Charge (e)
e.g. +0.310 for Si, −0.290 for O_NBO Fraction of electron charge on the atom. NOT the formal oxidation state. Source: force field or DFT Bader analysis.
substrate_atoms = [ {"element": "Si", "charge": +0.310, "position": [0.00, 0.00, 0.00], "label": "Si1_sub"}, {"element": "O", "charge": -0.290, "position": [0.00, 0.00, 1.60], "label": "O_NBO1_sub"}, ]

## Slide 7
How to Get Inputs — 3D Coordinates
Three routes from fastest to most accurate
Route A — Download + VESTA
1. Go to materialsproject.org 2. Search material → Download CIF 3. Open in VESTA → set Miller index 4. Add vacuum layer → Export POSCAR/XYZ 5. Load into library Time: ~10 minutes
Fastest Good for screening
Route B — ASE Slab Builder
from ase.build import surface, bulk, add_vacuum tio2 = bulk('TiO2', crystalstructure='rutile', a=4.594, c=2.958) slab = surface(tio2, (1,1,0), layers=4) add_vacuum(slab, 15.0) Time: ~20 minutes
Reproducible Scriptable
Route C — DFT Relaxation
1. Build initial slab (Route A or B) 2. Run VASP / Quantum ESPRESSO 3. Use final CONTCAR / output.xyz (true equilibrium positions) Time: hours–days on HPC
Most accurate For publications
Tip — Keep only surface layer atoms: surface_atoms = [a for a in all_atoms if a.position[2] >= z_max − 3.0]

## Slide 8
How to Get Inputs — Partial Charges
Charge ≠ Oxidation State
Why not use formal oxidation states? Si is +4 formally, but using +4 makes forces 167× too strong — simulations collapse. Partial charges reflect the real ~50% covalent nature of Si–O bonds. Si = +0.310 e because it retains 3.69 of 4 valence electrons.
Published Force Fields (Fastest, Good accuracy)
ClayFF → SiO₂, glass Si: +0.310, O_BO: −0.155, O_NBO: −0.290 Matsui–Akaogi → TiO₂ Ti5c: +0.580, O: −0.290 INTERFACE FF → Al₂O₃ Al: +0.480, O: −0.320 Look up: '[material] partial charge force field'
DFT Bader Analysis (Most accurate)
1. Run VASP with LAECHG=.TRUE. 2. bader CHGCAR -ref AECCAR0 -ref AECCAR2 3. Read ACF.dat (column 5 = Bader charge) Partial charge = valence electrons − Bader charge Quantum ESPRESSO: projwfc.x → Löwdin charges CP2K: MULLIKEN_POP keyword
Pymatgen BVAnalyzer (Rough, for quick screening)
from pymatgen.core import Structure from pymatgen.analysis.bond_valence import BVAnalyzer s = Structure.from_file('Al2O3.cif') bv = BVAnalyzer() s = bv.get_oxi_state_decorated_structure(s) Gives integer oxidation states (+3, −2) Not partial — use as last resort

## Slide 9
Formulas & Calculation Flow
Step-by-step inside the library
STEP 1
Group Dipole Moment
μ = Σᵢ qᵢ rᵢ
Sum of (charge × position) over all atoms. Outputs one vector per surface. Used as diagnostic — tells you if surfaces are polar.
STEP 2
Geometric Centroid
r̄ = (1/N) Σᵢ rᵢ
Unweighted mean position of all atoms. Used as origin for local dipoles. Makes all energies origin-independent.
STEP 3
Local Atomic Dipole
μᵢ = qᵢ (rᵢ − r̄)
Per-atom dipole relative to centroid. Captures each atom's individual contribution. Larger charge + farther from centroid = stronger dipole.
STEP 4
Pairwise Interaction Energy
U = 14.3996 × [μ₁·μ₂/r³ − 3(μ₁·r̂)(μ₂·r̂)/r³]
Applied to all N×M substrate–film pairs. 14.3996 = Coulomb constant in eV·Å/e². U < 0 → attractive, U > 0 → repulsive.
STEP 5
Rank & Filter
Sort by U (ascending) Apply distance cutoff
132 pairs sorted from most negative to most positive. Cutoff removes distant pairs (default 8 Å). Outputs ranked table with labels and types.

## Slide 10
Deep Dive — Why Si = +0.310 e and Not +4
Partial charge vs formal oxidation state
The Si–O Bond Is ~50% Covalent
Formal oxidation state: Si⁴⁺ → +4 This assumes 4 electrons fully transferred to O. Reality: Si–O is partly covalent. Electrons are shared, not transferred. Si retains 3.69 of 4 valence electrons → net charge = +0.310 e only. Using +4 would make forces 167× too strong. The 0.310 value comes from ClayFF force field (Cygan et al., J. Phys. Chem. B, 2004): → Quantum calc on SiO₄(OH)₄ cluster → ESP fitting to electron density → Charge balanced across 4 bonds: Si donates 0.31 e total Each BO gets 0.31/4 × 2 = 0.155 e → O_BO charge = −0.155 e ✓ NBO gets more → −0.290 e ✓
Electronegativity Drives the Charge
Bond ΔEN Partial charge on metal ────────────────────────────────────── Ti–O 1.90 Ti = +0.580 e (highest) Si–O 1.54 Si = +0.310 e B–O 1.40 B = +0.270 e H–O 1.24 H = +0.175 e (lowest) Larger ΔEN → more electrons pulled away → higher positive partial charge
Charge Balance Check (SiO₂ unit cell)
Si charge: +0.310 e × 1 = +0.310 e O charge: −0.155 e × 2 = −0.310 e ───────────────────────────────────── Net charge: = 0.000 e ✓ The unit cell is electrically neutral. Charges donated by Si exactly equal charges received by the two oxygens.

## Slide 11
Case Study — Borosilicate Glass vs. TiO₂ Thin Film
Real-world interface test
Interface Geometry (z-axis view)
z (Å) 5.8 ─ H_OH1_film (+0.18 e) 5.2 ─ O_OH1_film (−0.20 e) 4.5 ─ Ti6c1_film (+0.48 e) 4.2 ─ O_br_film (−0.29 e) 3.8 ─ O_ip_film (−0.26 e) 3.5 ─ Ti5c_film ★ (+0.58 e) ←── primary anchor ══════ interface gap ≈ 1.9 Å ══════ 1.6 ─ O_NBO_sub ★ (−0.29 e) ←── primary docking 0.8 ─ O_BO_sub (−0.155 e) 0.0 ─ Si_sub / B (+0.31 e) ↑ Film dipole (+z) ↓ Glass dipole (−z) Anti-parallel → macroscopic attraction
Glass Substrate — 12 atoms
Si × 3 +0.310 e Tetrahedral centres O_BO × 4 −0.155 e Bridging oxygens O_NBO × 3 −0.290 e Non-bridging (surface) B × 1 +0.270 e Borosilicate network H × 1 +0.175 e Silanol –OH
TiO₂ Film — 11 atoms
Ti5c × 3 +0.580 e 5-fold Ti (reactive) Ti6c × 1 +0.480 e 6-fold Ti (bulk-like) O_br × 3 −0.290 e Bridging O rows O_ip × 2 −0.260 e In-plane O O_OH × 1 −0.200 e Hydroxyl O H_OH × 1 +0.180 e Hydroxyl H
Total pairs to evaluate: 12 × 11 = 132

## Slide 12
Case Study Results — Dipole Moments & Unit Tests
Unit Test Results — All 6 Passed
✓
test_dipole_moments
Glass: 7.748 D | TiO₂: 13.463 D
✓
test_interaction_table_structure
132 pairs generated correctly
✓
test_best_interaction_attractive
Best = O_NBO1 – Ti5c1 at −2.224 eV
✓
test_distance_calculation
d = 1.9000 Å verified
✓
test_cutoff_filter
132 → 65 pairs at 4.5 Å cutoff
✓
test_energy_symmetry
U(A→B) = U(B→A) confirmed
Glass Dipole Moment
μx = −0.6184 e·Å μy = −0.1971 e·Å μz = −1.4768 e·Å ← dominant |μ| = 1.6131 e·Å = 7.748 Debye Net Q = −0.115 e Dipole points DOWN (−z) Negative charge at top of glass (NBO layer)
TiO₂ Film Dipole Moment
μx = −0.0592 e·Å μy = +0.9833 e·Å μz = +2.6240 e·Å ← dominant |μ| = 2.8028 e·Å = 13.463 Debye Net Q = +0.810 e Dipole points UP (+z) Positive Ti5c layer faces the glass
Anti-parallel dipoles → macroscopic attraction confirmed

## Slide 13
Case Study Results — Ranked Interaction Table
132 pairs sorted by energy — top 10 attractive + bottom 5 repulsive
Rank
Substrate Atom
Film Atom
Distance (Å)
Energy (eV)
Type
1
O_NBO1_sub
Ti5c1_film
1.9000
−2.2243
attractive
2
O_NBO3_sub
Ti5c3_film
2.4473
−0.3509
attractive
3
H_OH1_sub
Ti5c1_film
1.4980
−0.1875
attractive
4
H_OH1_sub
O_br1_film
1.9217
−0.1707
attractive
5
Si2_sub
O_br2_film
4.2455
−0.1227
attractive
6
O_NBO1_sub
Ti5c3_film
4.0451
−0.1217
attractive
7
O_BO3_sub
Ti5c3_film
2.9082
−0.1162
attractive
8
O_BO1_sub
Ti5c1_film
3.1385
−0.1040
attractive
9
Si2_sub
Ti5c2_film
4.0817
−0.1000
attractive
10
O_BO2_sub
Ti5c2_film
2.8276
−0.0996
attractive
128
O_NBO1_sub
O_ip1_film
2.7321
+0.1594
repulsive
129
O_NBO2_sub
Ti5c2_film
2.8320
+0.2178
repulsive
130
Si1_sub
Ti5c1_film
3.5000
+0.2451
repulsive
131
O_NBO3_sub
O_br3_film
2.8674
+0.2996
repulsive
132
O_NBO2_sub
O_br2_film
2.6729
+0.5704
repulsive
Total: 132 pairs | Attractive: 67 (50.8%) | Repulsive: 65 (49.2%) | Best: −2.2243 eV | Worst: +0.5704 eV

## Slide 14
Actionable Findings from the Case Study
What the ranked table tells the experimentalist
Finding 1
Dominant pair: O_NBO ↔ Ti5c at −2.224 eV
6.3× stronger than rank 2. Focus all surface engineering here. Action: Increase NBO density on glass by reducing B₂O₃ content or alkali leaching before deposition.
Finding 2
Ti5c is 50× more active than Ti6c
Ti5c ranks 1,2,3,6,7,8,9,10. Ti6c first appears at rank 21 (−0.045 eV). Action: Deposit TiO₂ under reduced O₂ pressure to maximise Ti5c surface density.
Finding 3
Surface –OH groups HELP adhesion
Silanol H contributes ranks 3 & 4 (−0.188 + −0.171 = −0.36 eV extra). Action: Wet-clean glass before deposition. Do not avoid hydroxylation.
Finding 4
O–O misregistry is the worst case (+0.570 eV)
O_NBO on glass directly above O_br on film → strongly repulsive. Action: Optimise in-plane rotation of film during deposition.
Finding 5
Library reduces DFT workload by 90–95%
132 pairs in <1 sec. Cutoff at 3 Å leaves ~10 high-priority DFT targets. Action: Run DFT only on top-ranked pairs identified here.

## Slide 15
Limitations & Future Work
Current Limitations
⚠ Fixed partial charges — no polarizability. Induction energy (~15–20% of rank-1 pair) not captured.
⚠ No dispersion / van der Waals (London C₆/r⁶) term included.
⚠ No charge–charge Coulomb term. Electrostatic monopole–monopole interaction not calculated.
⚠ Static model — no thermal motion, no solvent screening, no dynamics.
⚠ Accuracy depends on quality of input charges. Force-field charges ≈ good; formal oxidation states = rough.
Planned Future Work
→ Add polarizability (α) per element → includes induction energy term.
→ Integrate London dispersion (C₆/r⁶) for van der Waals contribution.
→ GUI / web interface for non-programmers.
→ Extend to liquid–solid interfaces (solvent screening factor ε).
→ Benchmark against experimental adhesion energy database for validation.
→ Auto-suggest deposition conditions based on ranked output.

## Slide 16
Conclusion
What was built
A production-ready Python library — 7 modules, pip-installable — that screens all substrate–film atom-pair interactions using dipole–dipole physics.
What it calculates
Group dipole moments, per-atom local dipoles, and pairwise interaction energies for all N×M atom combinations, ranked from most attractive to most repulsive.
What the Glass–TiO₂ test proved
O_NBO ↔ Ti5c is the dominant bonding pair at −2.224 eV — 6.3× stronger than rank 2. All 6 unit tests pass. Results match DFT literature expectations.
Why it matters
Reduces interface screening from 3–5 days of DFT to under 1 second. Gives experimentalists specific, actionable guidance on surface engineering.
github.com/shubhamgangwar-01/Surface-Dipole-Library